## Slide 1: The memory Hierarchy

## Slide 2: The Memory Hierarchy
Real systems have a several levels storage types:
  Top of hierarchy: Small and fast storage close to CPU
  Bottom of Hierarchy: Large and slow storage further from CPU
Caching is used to transfer data between different levels of the hierarchy.
To the programmer / compiler does not need to know
  The hardware provides an abstraction : memory looks like like a single large array.
But performance depends on program’s access pattern.

## Slide 3: The Memory Hierarchy

## Slide 4: Computer clusters extend the memory hierarchy
A data processing cluster is simply many computers linked through an ethernet connection.
Storage is shared
Locality: Data to reside on the computer will use it.
“Caching” is replaced by “Shuffling”
Abstraction is spark RDD.
Ethernet

## Slide 5: Sizes and latencies in a typical memory hierarchy.
 | CPU (Registers) | L1 Cache | L2 Cache | L3 Cache | Main Memory | Disk Storage | Local Area Network
Size (bytes) | 1KB | 64KB | 256KB | 4MB | 4-16GB | 4-16TB | 16TB – 10PB
Latency | 300ps | 1ns | 5ns | 20ns | 100ns | 2-10ms | 2-10ms
Block size | 64B | 64B | 64B | 64B | 32KB | 64KB | 1.5-64KB
12 orders of magnitude
6 orders of magnitude

## Slide 6: Summary
Memory Hierarchy: combining storage banks with different latencies.
Clusters: multiple computers, connected by ethernet, that share their storage.